## Slide 1: Troubleshooting

## Slide 2: Troubleshooting
This presentation will
Define troubleshooting.
Introduce the types of errors that may require troubleshooting.
Detail the logical steps required to troubleshoot a non-functional digital logic circuit.
Notes: Introductory Slide / Overview of Presentation

## Slide 3: Troubleshooting
Troubleshooting is the process you must undertake to isolate the source of a problem in a circuit that is not working, and then fix it.
This process is sometimes referred to as debugging. However, debugging typically applies to isolating a problem with software, whereas troubleshooting is typically associated with fixing hardware problems.
For this presentation we will focus on the troubleshooting process for digital electronics, both combinational and sequential.
Notes: A brief definition of troubleshooting.

## Slide 4: Sources of Problems
When you design and build a digital electronic circuit, three types of errors can occur.
  Design Error: With this error the circuit works perfectly as designed, but the design is incorrect and does not meet the design specifications.
  Build Error: With this error the circuit was designed properly, but was either built incorrectly or has a bad component.
  Design & Build Error: With this error the circuit was designed incorrectly AND was built wrong.
Fortunately, if you follow the design process to simulate and verify your design prior to building it, the third error type will not occur.
Regardless of the error type, design or build, the process of identifying the error and fixing it is the same: Divide and Conquer.
Notes: Sources of problems that require troubleshooting.

## Slide 5: Divide & Conquer – An Analogy
To illustrate the process of Divide & Conquer, consider the following analogy:
Draw a single card from a deck of playing cards and try to determine what the card is.
One approach would be to simply randomly guess any one of the 52 cards in the deck in no particular order. Clearly not a good idea.
Another approach would be to sequentially go through all 52 cards in the deck in order. This process would work, but it would be very tedious.
The best solution to the problem is the Divide & Conquer approach.
Notes: http://www.troubleshooters.com/utp/hesley.htm

## Slide 6: Divide & Conquer
Let’s assume the card is the 7 of diamonds. The Divide & Conquer approach works as follows . . .
  Q. Is the card a red suit or a black suit? (52 cards to 26)
  A. Red.
  Q. Is it a heart or a diamond? (26 cards to 13)
  A. Diamond
  Q. Is it a face card or a number card? (13 cards to 3 face or 10 numbered)
  A. Number
  Q. Is the number 5 or below? (10 cards to 5)
  A. No
  Q. Is the number odd or even? (5 card to 2 odd or 3 even)
  A. Odd (it must be the 7 or 9 of diamonds)
  Q. Is it the 9 of diamonds?
  A. No
  Solution: The card is the 7 of diamonds.
Notes: http://www.troubleshooters.com/utp/hesley.htm

## Slide 7: Divide & Conquer
In order to successfully troubleshoot a problem, you must be able to ask the right questions. The answers should guide to the solution.
So, how does this Divide & Conquer approach apply to digital electronics?
Notes: http://www.troubleshooters.com/utp/hesley.htm

## Slide 8: Troubleshooting Flowchart
TEST
Fully test the circuit to determine if it is working correctly.
Working?
Re-Create A Fault
(i.e., Apply an input that causes the output to be incorrect.)
Finished
Congratulations!
Correct the Problem
Divide & Conquer
Starting from the faulty output, work your way toward the inputs gate-by-gate until the problem is identified
YES
NO
Notes: Review the process for troubleshooting a digital logic circuit.