## Slide 1: 555 Timer

## Slide 2: 555 Timer
This presentation will
Introduce the 555 Timer.
Derive the characteristic equations for the charging and discharging of a capacitor.
Present the equations for period, frequency, and duty cycle for a 555 Timer Oscillator.
Going Further….
Detail the operation of a 555 Timer Oscillator.
Derive the equations for period, frequency, and duty cycle for a 555 Timer Oscillator.
Notes: Introductory Slide / Overview of Presentation

## Slide 3: What is a 555 Timer?
The 555 timer is an 8-pin IC that is capable of producing accurate time delays and/or oscillators.
In the time delay mode, the delay is controlled by one external resistor and capacitor.
In the oscillator mode, the frequency of oscillation and duty cycle are both controlled with two external resistors and one capacitor.
This presentation will discuss how to use a 555 timer in the oscillator mode.
Notes: Presents a brief overview of the 555 timer.

## Slide 4: Capacitor
A capacitor is an electrical component that can temporarily store a charge (voltage).
The rate that the capacitor charges/discharges is a function of the capacitor’s value and its resistance.
To understand how the capacitor is used in the 555 Timer oscillator circuit, you must understand the basic charge and discharge cycles of the capacitor.
Notes: Before we jump into the understanding how a 555 timer works, first we must understand the basics of how a capacitor charges and discharges.

## Slide 5: Capacitor Charge Cycle
Equation for Charging Capacitor
Capacitor is initially discharged.
Switch is moved to position A.
Capacitor will charge to +12 v.
Capacitor will charge through the 2 K resistor.
Notes: Simple capacitor charge/discharge circuit. This slide presents the equation for a charging capacitor. The students will not be expected to remember this equation.

## Slide 6: Capacitor Discharge Cycle
Equation for Discharging Capacitor
Capacitor is initially charged.
Switch is moved to position B.
Capacitor will discharge to +0 v.
Capacitor will discharge through the 3 K resistor.
Notes: Simple capacitor charge/discharge circuit. This slide presents the equation for a discharging capacitor. The students will not be expected to remember this equations.

## Slide 7: Capacitor Charge & Discharge
0 v
12 v
Switch has been at position B for a long period of time. The capacitor is completely discharged.
Switch is moved to position A. The capacitor charges through the 2K resistor.
Switch is moved back to position B. The capacitor discharges through the 3K resistors.
20 mSec
5 V
VC
Time
Notes: A complete charge and discharge cycle for the simple capacitor charge/discharge circuit.

## Slide 8: Block Diagram for a 555 Timer
Control Voltage (5)
Threshold Voltage (6)
Trigger Voltage (2)
Ground (1)
Vcc (8)
Discharge (7)
Reset (4)
Output (3)
-
+
-
+
RESET
SET
Q
Q
COMP1
COMP2
Flip-Flop
T1
Notes: Block diagram for the 555 timer.

## Slide 9: Schematic of a 555 Timer in Oscillator Mode
5 Volts
N/C
N/C
Discharge
Threshold /
Trigger
Ground
Output
1.666 V
3.333 V
RA
RB
C
Notes: Schematic of the 555 time configured as a oscillator. The grayed out area is the internal circuitry of the 555 timer. The external components RA, RB, & C are used to select the frequency and duty-cycle of the output waveform. In this examples the output is connected to a simple LED with a current limiting resistor.

## Slide 10: 555 Timer Design Equations
tHIGH : Calculations for the Oscillator’s HIGH Time
 |  |  |  |  |  |  | 5v
 |  |  |  |  |  |  | 3.333 v
Vc |  |  |  |  |  |  | 1.666 v
 |  |  |  |  |  |  | 0 v
 |  |  |  | tHIGH |  |  | 
Output |  |  |  |  |  |  | HIGH LOW
The Output Is HIGH While The Capacitor Is Charging Through RA + RB.
Notes: Derivation of the equation for t-HIGH.

## Slide 11: 555 Timer Design Equations
tLOW : Calculations for the Oscillator’s LOW Time
 |  |  |  |  |  |  | 5v
 |  |  |  |  |  |  | 3.333 v
Vc |  |  |  |  |  |  | 1.666 v
 |  |  |  |  |  |  | 0 v
 |  |  | tLOW |  |  |  | 
Output |  |  |  |  |  |  | HIGH LOW
The Output Is LOW While The Capacitor Is Discharging Through RB.
Notes: Derivation of the equation for t-LOW.

## Slide 12: 555 Timer – Period / Frequency / DC
Period:
Frequency:
Duty Cycle:
Notes: Summary of a 555 time design equations.

## Slide 13: Example: 555 Oscillator
Example:
  For the 555 Timer oscillator shown below, calculate the circuit’s, period (T), frequency (F), and duty cycle (DC).
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next slide.

## Slide 14: Example: 555 Oscillator
Solution:
Period:
Frequency:
Duty Cycle:
Notes: Here is the solution. If you print handouts, don’t print this page.

## Slide 15: Example: 555 Oscillator
Example:
  For the 555 Timer oscillator shown below, calculate the value for RA & RB so that the oscillator has a frequency of 2.5 KHz @ 60% duty cycle.
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next two slides.

## Slide 16: Example: 555 Oscillator
Solution:
Frequency:
Duty Cycle:
Two Equations & Two Unknowns!
Notes: Here is the solution. If you print handouts, don’t print this page.

## Slide 17: Example: 555 Oscillator
Solution:
Frequency:
Duty Cycle:
Substitute and Solve for RB
Substitute and Solve for RA
Notes: Here is the solution. If you print handouts, don’t print this page.

## Slide 18: Going Further…
555 Oscillator
Detail Analysis

## Slide 19: Detail Analysis of a 555 Oscillator
 |  |  |  |  |  |  |  | 5v
 |  |  |  |  |  |  |  | 3.333 v
Vc |  |  |  |  |  |  |  | 1.666 v
 |  |  |  |  |  |  |  | 0 v
RESET |  |  |  |  |  |  |  | HIGH LOW
SET |  |  |  |  |  |  |  | HIGH LOW
 |  |  |  |  |  |  |  | HIGH LOW
T1 |  |  |  |  |  |  |  | ON OFF
Q |  |  |  |  |  |  |  | HIGH LOW
Notes: Analysis of a 555 Oscillator: Slide 1 of 4

## Slide 20: Detail Analysis of a 555 Oscillator
 |  |  |  |  |  |  |  | 5v
 |  |  |  |  |  |  |  | 3.333 v
Vc |  |  |  |  |  |  |  | 1.666 v
 |  |  |  |  |  |  |  | 0 v
RESET |  |  |  |  |  |  |  | HIGH LOW
SET |  |  |  |  |  |  |  | HIGH LOW
 |  |  |  |  |  |  |  | HIGH LOW
T1 |  |  |  |  |  |  |  | ON OFF
Q |  |  |  |  |  |  |  | HIGH LOW
Notes: Analysis of a 555 Oscillator: Slide 2 of 4

## Slide 21: Detail Analysis of a 555 Oscillator
 |  |  |  |  |  |  |  | 5v
 |  |  |  |  |  |  |  | 3.333 v
Vc |  |  |  |  |  |  |  | 1.666 v
 |  |  |  |  |  |  |  | 0 v
RESET |  |  |  |  |  |  |  | HIGH LOW
SET |  |  |  |  |  |  |  | HIGH LOW
 |  |  |  |  |  |  |  | HIGH LOW
T1 |  |  |  |  |  |  |  | ON OFF
Q |  |  |  |  |  |  |  | HIGH LOW
Notes: Analysis of a 555 Oscillator: Slide 3 of 4

## Slide 22: Detail Analysis of a 555 Oscillator
 |  |  |  |  |  |  |  | 5v
 |  |  |  |  |  |  |  | 3.333 v
Vc |  |  |  |  |  |  |  | 1.666 v
 |  |  |  |  |  |  |  | 0 v
RESET |  |  |  |  |  |  |  | HIGH LOW
SET |  |  |  |  |  |  |  | HIGH LOW
 |  |  |  |  |  |  |  | HIGH LOW
T1 |  |  |  |  |  |  |  | ON OFF
Q |  |  |  |  |  |  |  | HIGH LOW
Output Is LOW While The Capacitor Is Discharging Through RB.
Output Is HIGH While The Capacitor Is Charging Through RA + RB.
Notes: Analysis of a 555 Oscillator: Slide 4 of 4

## Slide 23: 555 Timer Design Equations
tHIGH : Calculations for the Oscillator’s HIGH Time
Notes: Derivation of the equation for t-High.

## Slide 24: 555 Timer Design Equations
tLOW: Calculations for the Oscillator’s LOW Time
Notes: Derivation of the equation for t-Low.

## Slide 25: 555 Timer – Period / Frequency / DC
Period:
Frequency:
Duty Cycle:
Notes: Summary of a 555 time design equations.